## Slide 1: Introduction to pathogen sequencing on the Illumina platform
Laboratory Module

## Slide 2: Genomic epidemiology workflow
Pixel True https://www.pixeltrue.com/about, CC BY-SA 4.0, via Wikimedia Commons
BioRender.com

## Slide 3: Outline
Using pathogen genomes for epidemiology
Sequencing approaches
  Unbiased vs targeted approaches
Sequencing technologies
  Brief overview of sequencing platforms
  Illumina sequencing

## Slide 4: Using pathogen genomes for epidemiology
DNA sequencing is increasingly used for infectious disease surveillance and to answer public health questions
Genomic epidemiology uses the mutations that appear over time in pathogen genomes to infer the likely spread and incidence of a pathogen

## Slide 5: Using pathogen genomes for epidemiology
Phylogenetic tree
DNA sequencing is increasingly used for infectious disease surveillance and to answer public health questions
Genomic epidemiology uses the mutations that appear over time in pathogen genomes to infer the likely spread and incidence of a pathogen

## Slide 6: Using pathogen genomes for epidemiology
Analyze and interpret genome sequences with support of real time, scalable tools
https://nextstrain.org/ncov/global

## Slide 7: Using pathogen genomes for epidemiology
Share sequences and interpretation through online platforms
https://virological.org

## Slide 8: Using pathogen genomes for epidemiology
Other methods for molecular characterization of pathogens:
Rapid diagnostic tests
PCR-based assays / CRISPR-based assays

## Slide 9: Using pathogen genomes for epidemiology
Other methods for molecular characterization of pathogens:
Rapid diagnostic tests
PCR-based assays / CRISPR-based assays
ATGCAGCTAGCTGATGCTGACTGACTGACTGCTGATTCGCTAATCGTACCTCGACGATCAT

## Slide 10: Using pathogen genomes for epidemiology
Other methods for molecular characterization of pathogens:
Rapid diagnostic tests
PCR-based assays / CRISPR-based assays
Multi-locus variable typing (MLVA) – bacterial genomes
Multi-locus sequence typing (MLST) – bacterial genomes
Single amplicon sequencing – e.g., 16S for bacteria or marker gene for viruses
ATGCAGCTAGCTGATGCTGACTGACTGACTGCTGATTCGCTAATCGTACCTCGACGATCAT

## Slide 11: Using pathogen genomes for epidemiology
ATGCAGCTAGCTGATGCTGACTGACTGACTGCTGATTCGCTAATCGTACCTCGACGATCAT
Full length pathogen genomes provide the most comprehensive picture of pathogen variation
Other methods for molecular characterization of pathogens:
Rapid diagnostic tests
PCR-based assays / CRISPR-based assays
Multi-locus variable typing (MLVA) – bacterial genomes
Multi-locus sequence typing (MLST) – bacterial genomes
Single amplicon sequencing – e.g., 16S for bacteria or marker gene for viruses

## Slide 12: Using pathogen genomes for epidemiology
Gardy et al. 2011 NEJM
Full length pathogen genomes provide the most comprehensive picture of pathogen variation

## Slide 13: Outline
Using pathogen genomes for epidemiology
Sequencing approaches
  Unbiased vs targeted approaches
Sequencing technologies
  Brief overview of sequencing platforms
  Illumina sequencing

## Slide 14: How can we generate pathogen sequences?
There are many options & variations for each of these steps
Your sample type, study goal and & resources should guide your choice
Created with BioRender.com

## Slide 15: How can we generate pathogen sequences?
Many kits and methods available to extract RNA and/or DNA
  Include precipitation, column-based, and bead-based methods
Your starting material will impact what you can sequence
  Many viruses (e.g., Lassa, Ebola, SARS-CoV-2) have RNA genomes
Created with BioRender.com
Notes: Add biorender citation?

## Slide 16: How can we generate pathogen sequences?
Many different approaches for preparing DNA libraries
* If you are starting with RNA you will need to convert this to cDNA before preparing DNA libraries
*
Created with BioRender.com

## Slide 17: How can we generate pathogen sequences?
Many different approaches for preparing DNA libraries
Sensitivity, speed
Unbiased, accuracy
Metagenomic sequencing
Amplicon-based sequencing
Created with BioRender.com

## Slide 18: Overview of sequencing approaches
Unbiased (sometimes called metagenomic) sequencing captures all genetic material in a sample
Does not require prior knowledge of what organisms are in the sample
More expensive and requires more time than many targeted sequencing approaches
Sensitivity, speed
Unbiased, accuracy
Metagenomic sequencing
Amplicon-based sequencing

## Slide 19: Overview of sequencing approaches
Sensitivity, speed
Unbiased, accuracy
Metagenomic sequencing
Uses primers to specifically amplify genome of interest (usually in many overlapping short pieces)
More sensitive, especially for low-input samples. Faster and cheaper than unbiased methods
Requires prior knowledge of the target pathogen and its genome sequence.
Can be susceptible to contamination and PCR bias
Amplicon-based sequencing

## Slide 20: Overview of sequencing approaches
Sensitivity, speed
Unbiased, accuracy
Metagenomic sequencing
Amplicon-based sequencing

## Slide 21: Considerations for selecting an approach
Do you know what pathogen you are looking for?
Are you looking for one pathogen or many?
Is this pathogen well-described (e.g., published genomes)?
Do you know what the viral load in your sample is (e.g., Ct value)?
What is the goal of your study (e.g., phylogenetics or just detection)

## Slide 22: Outline
Using pathogen genomes for epidemiology
Sequencing approaches
  Unbiased vs targeted approaches
Sequencing technologies
  Brief overview of sequencing technologies
  Illumina sequencing

## Slide 23: How can we generate pathogen sequences?
Created with BioRender.com

## Slide 24: Which technology should I use to sequence?
Massively parallel sequencing
(”next” or “second” generation sequencing)
High throughput (millions or billions of reads)
Short reads (<500nt “read” per DNA module)
High fidelity
Large, expensive, and sensitive machines
Example platforms:
  Roche 454, Illumina, Ion Torrent
Single molecule sequencing
(also called “long read” sequencing)
Medium throughput, optimized for real-time
Long reads (>100kb possible)
Medium fidelity
Low cost, portable machines
Example platforms:
  Oxford Nanopore, PacBio
Created with BioRender.com

## Slide 25: Illumina sequencing: how it works
MiSeq V2 Nano flowcell

## Slide 26: Illumina sequencing: how it works
Short DNA fragments bind to oligos on the surface of the flowcell
Created with BioRender.com

## Slide 27: Illumina sequencing: how it works
“Bridge amplification” makes many copies of a fragment to amplify signal (cluster)
Created with BioRender.com

## Slide 28: Illumina sequencing: how it works
Labelled nucleotides are washed over the flowcell and incorporated where they reflect the next base in the sequence
The flowcell is imaged to determine which nucleotide was incorporated in each cluster before the process begins again
Created with BioRender.com

## Slide 29: Illumina sequencing: how it works
Fluorescent intensities are converted to base calls and output for analysis
Created with BioRender.com

## Slide 30: Illumina sequencing: how it works
Created with BioRender.com

## Slide 31: Range of instruments on the Illumina platform
Benchtop box
Large, free-standing
Pool 10s of samples
Pool 1000s of samples
$100s per run
$10,000s per run
Created with BioRender.com

## Slide 32: iSeq and MiSeq are widely used for pathogens
iSeq
MiSeq
Up to 4 million reads per run
9.5 – 19 hours to run
Up to 2x150 bp reads
Kits cost $500-$600 USD
5-25 million reads per run
4-48 hours to run
Up to 2x300 bp reads
Kits cost $1,000-$1,400 USD
Created with BioRender.com

## Slide 33: Summary
Pathogen genomes give us more complete information for inferring epidemiology than other molecular tools
When deciding how to sequence a sample we need to select an approach as well as a sequencing platform
Illumina sequencing is a widely used platform for pathogen sequencing at medium to high throughput