## Slide 1: Sequencing protocol overview
Laboratory Module

## Slide 2: Genomic epidemiology workflow
Pixel True https://www.pixeltrue.com/about, CC BY-SA 4.0, via Wikimedia Commons
BioRender.com

## Slide 3: Conceptual overview of protocol

## Slide 4: Outline
Minimizing inter-sample contamination
Working with temperature-sensitive materials
Using thermocyclers
Reagent handling
Sample pooling

## Slide 5: Conceptual overview of protocol

## Slide 6
Protocol Step
Amplicon PCR clean up
Sequencing
cDNA prep
Amplicon PCR
Library indexing PCR
Library PCR clean up
Library quant and pooling
Extraction

## Slide 7
Protocol Step
DNA- and RNA-free reagent preparation work space
Prepare in ‘clean’ work space (e.g. hood or bench) and transfer to other work spaces for sample loading
Amplicon PCR clean up
Sequencing
cDNA prep
Amplicon PCR
Library indexing PCR
Library PCR clean up
Library quant and pooling
Extraction

## Slide 8
Pre-PCR
Protocol Step
DNA- and RNA-free reagent preparation work space
Appropriate biosafety level laboratory
Prepare in ‘clean’ work space (e.g. hood or bench) and transfer to other work spaces for sample loading
Amplicon PCR clean up
Sequencing
cDNA prep
Amplicon PCR
Library indexing PCR
Library PCR clean up
Library quant and pooling
Extraction
Sample handling work space

## Slide 9
Pre-PCR
Protocol Step
DNA- and RNA-free reagent preparation work space
Appropriate biosafety level laboratory
Prepare in ‘clean’ work space (e.g. hood or bench) and transfer to other work spaces for sample loading
Amplicon PCR clean up
Sequencing
cDNA prep
Amplicon PCR
Library indexing PCR
Library PCR clean up
Library quant and pooling
Extraction
Sample handling work space
RNA extract and cDNA work space (e.g. hood in separate room)

## Slide 10
Pre-PCR
Post-PCR
Amplicon work space (e.g. hood)
Protocol Step
DNA- and RNA-free reagent preparation work space
Appropriate biosafety level laboratory
Prepare in ‘clean’ work space (e.g. hood or bench) and transfer to other work spaces for sample loading
Amplicon PCR clean up
Sequencing
cDNA prep
Amplicon PCR
Library indexing PCR
Library PCR clean up
Library quant and pooling
Extraction
Sample handling work space
RNA extract and cDNA work space (e.g. hood in separate room)

## Slide 11
Pre-PCR
Post-PCR
Amplicon work space (e.g. hood)
Protocol Step
DNA- and RNA-free reagent preparation work space
Library work space (e.g. hood)
RNA extract and cDNA work space (e.g. hood in separate room)
Appropriate biosafety level laboratory
Prepare in ‘clean’ work space (e.g. hood or bench) and transfer to other work spaces for sample loading
Amplicon PCR clean up
Sequencing
cDNA prep
Amplicon PCR
Library indexing PCR
Library PCR clean up
Library quant and pooling
Extraction
Sample handling work space

## Slide 12: Summary: Essential laboratory workspaces
Work space | Description
Clean area | Nucleic acid-free area for preparation of mastermixes, reaction tubes, reaction plates, etc. prior to sample loading.
Pre-PCR area | Area for handling viral RNA extracts and cDNA prior to multiplex amplicon PCR step.
Post-PCR area* | Area for handling amplicon and library PCR products. Can optionally be split into separate work spaces for amplicon and library products.
*Amplicon products are high concentration and pose a high contamination risk

## Slide 13: Minimizing inter-sample contamination
Seal samples tightly to prevent contamination, especially prior to long-term storage and thermocycler reactions
Always centrifuge plates and strips prior to opening
Make sure tips are tightly attached to active pipettes before loading sample
Aliquot longer-lasting reagents such as primer pools, SPRI beads, and enzyme master mixes
Use NTCs and spike-ins to check for contamination in final library

## Slide 14: Outline
Minimizing inter-sample contamination
Working with temperature-sensitive materials
Using thermocyclers
Reagent handling
Sample pooling

## Slide 15: Working with temperature-sensitive materials
RNA is very volatile compared to DNA, so ensure that all RNA is kept cold at all times
Other temperature-sensitive reagents include: reverse transcriptase and DNA polymerase enzymes
Reduce the number of freeze-thaw cycles whenever possible

## Slide 16: Summary: reagent storage temperatures
Storage temperature | Materials
-80˚C | Viral RNA extracts
-20˚C | PCR enzymes, primers, dsDNA (long term storage)
4˚C | SPRI beads, dsDNA (short-term storage)
~0˚C (ice buckets, ice blocks) | Temperature-sensitive reagents and samples in active use (e.g. during PCR preparation)
Room temperature | Ethanol, water

## Slide 17: Optimizing thermocycler performance
Pre-heat thermocyclers during reaction preparation (e.g. sample loading step) if needed
Include at least 3 total 8-strips of tubes to equilibrate thermocycler lid pressure (empty “BALANCE” tubes OK) if using 8-strip tubes in thermocyclers
Avoid leaving samples on thermocyclers for long periods following the completion of PCR programs

## Slide 18: Outline
Minimizing inter-sample contamination
Working with temperature-sensitive materials
Using thermocyclers
Reagent handling
Sample pooling

## Slide 19: Proper reagent handling can improve results
Prepare mastermixes for a greater number of samples than theoretically needed to account for volume loss via pipetting and calibration issues
Prepare 80% EtOH solution for SPRIs on the same day the SPRIs are performed to prevent evaporation-driven decreases in EtOH content

## Slide 20: Outline
Minimizing inter-sample contamination
Working with temperature-sensitive materials
Using thermocyclers
Reagent handling
Sample pooling

## Slide 21: Pooling samples for even sequencing coverage
Maximum volume | 30 µL
Number of samples to pool | 3
Maximum volume per sample | ______ µL
Average sample concentration | 0.5 ng/µL
Target DNA amount | ______ ng

## Slide 22: Pooling samples for even sequencing coverage
Maximum volume | 30 µL
Number of samples to pool | 3
Maximum volume per sample | 10 µL
Average sample concentration | 0.5 ng/µL
Target DNA amount | ______ ng

## Slide 23: Pooling samples for even sequencing coverage
Maximum volume | 30 µL
Number of samples to pool | 3
Maximum volume per sample | 10 µL
Average sample concentration | 0.5 ng/µL
Target DNA amount | 5 ng

## Slide 24: Pooling samples for even sequencing coverage
Batch | Sample name | Barcode | Volume to pool | Amount in pool
1 | Sample 1 | 1 ng/µL | ______ µL | ______ ng
1 | Sample 2 | 0.1 ng/µL | ______ µL | ______ ng
1 | Sample 3 | 0.5 ng/µL | ______ µL | ______ ng

## Slide 25: Pooling samples for even sequencing coverage
Batch | Sample name | Barcode | Volume to pool | Amount in pool
1 | Sample 1 | 1 ng/µL | 5 µL | 5 ng
1 | Sample 2 | 0.1 ng/µL | 50 µL | 5 ng
1 | Sample 3 | 0.5 ng/µL | 10 µL | 5 ng

## Slide 26: Pooling samples for even sequencing coverage
Batch | Sample name | Barcode | Volume to pool | Amount in pool
1 | Sample 1 | 1 ng/µL | 5 µL | 5 ng
1 | Sample 2 | 0.1 ng/µL | 50 µL | 5 ng
1 | Sample 3 | 0.5 ng/µL | 10 µL | 5 ng

## Slide 27: Pooling samples for even sequencing coverage
Batch | Sample name | Barcode | Volume to pool | Amount in pool
1 | Sample 1 | 1 ng/µL | 5 µL | 5 ng
1 | Sample 2 | 0.1 ng/µL | 10 µL | 1 ng
1 | Sample 3 | 0.5 ng/µL | 10 µL | 5 ng
 |  | Total Vol. | 25 µL | 

## Slide 28: Calculating pool molarity
Tapestation or BioAnalyzer measurement
(SARS-CoV-2 tiled amplicon scheme fragment size typically ~450 bp)
QuBit measurement

## Slide 29: Summary
Minimize contamination across samples through work space separation and other best practices
Keep materials like DNA, RNA, and enzymes at specified temperatures
Prepare reagents in quantities that account for inevitable volume loss
Pool equal amounts of samples to achieve even coverage during sequencing